## Slide 1: Automatic LED Light Control System
Here is where your presentation begins

## Slide 2
This presentation is about our project called "Automatic LED Light Control System Using LDR and Arduino." It is a capstone project report submitted to Saveetha School of Engineering, SIMATS, Chennai, for our Bachelor of Engineering in Computer Science & Engineering. The project was done by Parthasarathy V, Vasanth K, and Kathiravan, under the guidance of our course faculty, Dr. Anbuselvan N. The work was completed in March 2025 to show how technology can help save energy.

## Slide 3: Project Overview

## Slide 4: Project Overview
Our project focuses on making a smart LED light system that saves energy. We used a Light Dependent Resistor, or LDR, to measure the light around it and an Arduino to control how bright the LED gets. When it’s bright outside, like during the day, the system dims or turns off the LED. When it’s dark, like at night, it makes the LED brighter for safety. We tested this idea using Tinker cad software, and it proved that our system can save energy, reduce costs, and help the environment by lowering pollution. This makes it a good fit for sustainable cities.

## Slide 5: Why This Project Matters
Street lights are very important because they keep people safe at night, but the old systems use too much energy. Traditional lights stay fully bright all night, even when they don’t need to be, which wastes power and costs more money. Now, LEDs are a better choice because they use less energy and can change brightness. Our project aims to create a system that uses an LDR and Arduino to control LED lights smartly, saving energy while still keeping streets safe and well-lit.

## Slide 6: The Problem and Objective

## Slide 7: The Problem and Objective
Old street lights cause a big problem because they use too much energy. They stay bright all night, even when there’s enough light from the moon or other sources, which wastes power. This increases electricity bills, adds to pollution, and harms the environment. It affects cities that pay for the lights, taxpayers who fund them, and nature that suffers from extra light and energy use. Our project tries to solve this by making a system that only uses power when it’s really needed.
The main goal of our project is to design a smart street light system that uses less energy. We wanted to use an LDR to sense changes in light around it and an Arduino to adjust the LED brightness automatically. By doing this, we aimed to prove that our system can save energy through a simulation. Another important goal was to support the idea of smart and green cities by reducing power use and making street lighting more efficient for the future.

## Slide 8: System Design and Outcomes
How It Works
Steps We Followed
Our system is built with simple parts like an LDR, an Arduino, an LED, and some resistors. The LDR checks how bright it is outside by changing its resistance—less resistance in bright light and more in the dark. The Arduino reads this change and decides how bright the LED should be. We tested the whole setup in Tinker cad to see if it works properly. This way, the LED gets brighter only when it’s dark and dims when there’s enough light, saving energy.
To make this project, we followed clear steps. First, we picked the right parts, like the Arduino and LDR, to build our system. Then, we connected them into a circuit so they could work together. After that, we wrote a program for the Arduino to control the LED based on the LDR’s readings. We tested everything in Tinker cad by changing the light levels to see how the system reacts. Finally, we looked at the results and made improvements to ensure it works well.
Our tests showed that the system works as planned. The LDR’s resistance goes down when there’s more light and up when it’s darker. Based on this, the Arduino adjusts the LED—making it bright in the dark and dim in the light. This saves energy compared to old lights that stay on all the time. We made tables to show how the LDR readings match the LED brightness, proving that our idea can reduce power use effectively.
What We Found

## Slide 9: System Details
The system has a simple circuit where the LDR and LED are connected to the Arduino. The LDR senses light, and the Arduino uses a program to read its value and set the LED’s brightness. For example, when it’s very bright outside, the LED uses less power or turns off. When it’s dark, the LED shines at full power. We used something called PWM in the code to smoothly change the brightness, making the system both simple and smart.

## Slide 10: Project Insights and Impact
Why It’s Useful
What We Learned
This project is helpful because it saves energy, which lowers electricity bills for cities. It also reduces pollution and the carbon footprint, making it good for the environment. The system is affordable and easy to set up, so it can be used in many places. Plus, it fits into plans for smart cities, where technology makes life better and more sustainable. This makes our solution practical and valuable.
Doing this project taught us a lot. We learned how sensors like the LDR work and how to design circuits that use them. We got better at programming the Arduino to solve real problems. It also improved our skills in fixing issues and testing ideas. These lessons will help us in future engineering work and showed us how technology can make a difference.
While working on this project, we faced some issues. The Tinker cad software we used couldn’t perfectly show how the LDR and LED behave, so we had to simplify things. It also took time to figure out the best way to match LDR readings with LED brightness. For the future, we think using better software, adding features like motion sensors, or testing it in real life could make the system even better and more accurate.
Challenges Faced

## Slide 11: Flowchart Explanation
This slide explains the flowchart of our Automatic Light Brightness Controller. The process starts by setting up the system. The Arduino initializes the LED pin (D9) as an output to control the light and begins serial communication to send data for monitoring. Next, the Arduino reads the LDR value from pin A0, which gives a number between 0 and 1023 based on the light intensity around it. After that, the LDR value is mapped to a PWM range of 0 to 255, which decides how bright the LED should be. The Arduino then sets the LED brightness by sending this PWM value to the LED pin using the analogWrite function. To help with debugging, the system prints the LDR and PWM values on the Serial Monitor. Then, it waits for 200 milliseconds to avoid flickering or errors. Finally, the process loops back and repeats, continuously checking the light and adjusting the LED brightness as needed.

## Slide 12: Evaluation of Result

## Slide 13: Evaluation of Result
Light Intensity (Lux) | LDR Resistance (Ω)
0 (Complete Darkness) | 1,00,000
50 | 50,000
100 | 25,000
200 | 12,000
300 | 8,000
400 | 6,000
500 | 4,500
600 | 3,500
700 | 2,800
800 | 2,000
900 | 1,500
1000 (Bright Daylight) | 1,000
LDR Resistance vs. Light Intensity Table
LDR Resistance (Ω) | Light Intensity (Lux) | LED Brightness (0-255 PWM)
1,00,000 | 0 | 255 (Max Brightness)
50,000 | 50 | 230
25,000 | 100 | 200
12,000 | 200 | 160
8,000 | 300 | 120
6,000 | 400 | 90
4,500 | 500 | 70
3,500 | 600 | 50
2,800 | 700 | 30
2,000 | 800 | 15
1,500 | 900 | 5
1,000 | 1000 | 0 (LED OFF)
LED Brightness vs. LDR Resistance and Light Intensity Table

## Slide 14: Evaluation of Result

## Slide 15: Conclusion

## Slide 16: Conclusion
In the end, our project successfully created a smart LED light system that saves energy. The simulation proved it works well, adjusting brightness based on light levels, and it’s ready for real-world use. It helps build eco-friendly and smart cities by cutting down on power waste and pollution. This is a small but important step toward using technology for a greener future.

## Slide 17: Thanks
Please keep this slide for attribution
We want to thank everyone who helped us with this project. A special thanks goes to Dr. Anbuselvan N for guiding us and giving great advice. We are grateful to Saveetha School of Engineering for giving us the chance to work on this. The support from our faculty and coordinators made it possible to finish this project successfully.